$(h1ii47$)	Cubicle system E-BASIC$(kurz9Partition Wall System Type C$)

KEMMLIT UK
Bays Platt
Skirmett

Henley on Thames

Oxfordshire

RG9 6TD
Telephone: 01491 638606
info@kemmlituk.com - www.kemmlituk.com

# Construction

Steel composite elements, 30 mm thick, hot-galvanised,

static connection and vandal-resistant hardware.

TÜV-approved (GS seal of approval).

Options:
Type E-BASIC 1.1: Anodised profiles.
Type E-BASIC 1.2: Powder-coated profiles.

Height:
2000 mm, incl. 150 mm under panel clearance.
 
Partitions and pilasters (front panels):
Steel composite elements, 30 mm thick, hot-galvanised

S 250 GD + Z-275 according to DVV and DIN EN 10142,

respectively DIN EN 10147 as well as DIN EN 10143.

Visible varnish coating made of polyester, approx. 25 (m

thick. Additional protective varnish on the inside, 7-10 (m,

colour: white/grey coated.

The steel sheets are canted on all four sides. The inside

of the panels is filled with a warp-resistant inlay.

Screw-proof inlays guarantee a permanent and solid

mounting of accessories.

Profiles:
All profiles are made of aluminium and rounded (2 mm radius)

to reduce the risk of injuries. Warp-resistant stabiliser

head rail (55/43 mm) placed above the front is oval and

elegantly rounded.

As an option also in a rectangular shape (42/43 mm).

Wall-connection profiles made of U-channels

to allow minor adjustments for tolerances on site.

Supporting legs:

Made of corrosion-free aluminium (Ø 20mm).

Satin anodised or power-coated, with stainless steel

core and stainless steel floor plate. Durable cover sleeve

made of colour-coordinated nylon. Cover sleeve can easily

be lifted for cleaning purposes. Force-fit connection

by means of M12 screw connection to the hinge and

door stop profile.

As an option made entirely of stainless steel (Ø 20 mm).
Continuous height adjustability. Force-fit connection by

means of M12 screw connection to the hinge and door

stop profiles. Stainless steel cover sleeve can easily be

lifted for cleaning purposes.

Doors:
Steel composite elements, 30 mm thick, hot galvanised

(same construction as partitions and front panels/pilasters),

with integrated vertical aluminium profiles. The door stop

profiles made of aluminium, with integrated sound absorption.

Furniture/hardware:

1) Hinges:

2 robust 2–roller rising-butt edge hinges (Ø 20 mm) for

self-closing doors made of aluminium, satin anodised

or powder coated.

2) Furniture:

Single latch WC lock. Door knobs, red/white indicator

bolt with emergency release mechanism made

of satin anodised aluminium, stainless steel or impact

and shatter-resistant nylon.

Furniture/hardware options:

1) Hinges:

2 robust 2 -roller-edge hinges (Ø 20 mm) made of

aluminium satin anodised or powder coated, as an

option also in stainless steel.

2) Furniture:

Double latch WC lock. Safety lever handles (Ø 23 mm).

Red/white indicator bolt with emergency release mechanism

made of satin anodised aluminium, stainless steel or impact

and shatter resistant nylon.

Colours:
Partitions, pilasters and doors are available in white

(RAL 9010) and grey (RAL 7035). Profiles, hardware,

supporting legs, and accessories available in the same

colours according to the KEMMLIT colour chart (at

least 6 colours).

Environmental friendliness:
	Only environmentally friendly materials may be used,

without PVC’s or CFC‘s.

All prices ex works in Dusslingen. Taxes and duties

are unpaid, materials only. Installation and transportation

are not included.

47.10$)	                                                                                        $(menge0,000$) no.$(einhno.$)	$(d276$)$(ep.............$)	$(gb.............$)$(langAccessories for toilet cubicles $)

Accessories for toilet cubicles:

/E

KEMMLIT door stopper hooks made

of nylon 301

$$NNN

$(h1ii47.20$)	                        $(menge0,000$) no.$(einhno.$)	$(d276$)$(ep.............$)	$(gb.............$)$(langAccessories for toilet cubicles $)
 $)/E

$(langKEMMLIT wall hooks made of nylon 302

$)

$$NNN

$(h1ii47.30$)	                        $(menge0,000$) $(einh no.$)	$(d276$)$(ep.............$)	$(gb.............$)

/E

KEMMLIT paper roll holder made of

nylon 308

$$NNN

$(h1ii47.40$)	                        $(menge0,000 $)$(einh no.$)$(d276$)	$(ep.............$)	$(gb.............$)

$(langKEMMLIT replacement paper roll holder made

of nylon 309$)$(lang$)/E

$$NNN

$(h1ii47.50$)	                        $(menge0,000$) $(einh no.$)	$(d276$)$(ep............$)	$(gb.............$)

KEMMLIT WC-brush set, square-shaped, made

of nylon 310/E

$$NNN

$(h1ii47.60$)	                        $(menge0,000$) $(einh no.$)	$(d276$)$(ep.............$)	$(gb.............$)

$(lang
Accessories also available in stainless steel.$)

$)/E

$$GRUEnd

----------------------

Cubicle system$(kurz9Partition Wall system Type E-BASIC$)	$(gb.............$)

============

/E